Keep this notice near your VHF DSC Radio

VESSEL NAME

…………..………………….
MMSI …....….......…...…...…....
CALL SIGN ......…....….…..
PAN PAN
ONLY TO BE USED IN THE CASE OF URGENT MESSAGE CONCERNING THE SAFETY OF A VESSEL OR PERSON, BUT WHERE IMMEDIATE ASSISTANCE IS NOT REQUIRED, SUCH AS MEDICAL ADVICE OR REQUIRING A TOW.
1. Ensure radio is switched on.
2. Press CALL or MENU button.
3. Press ALL SHIPS button.
4. Select URGENCY CALL.
5. Press SEND button.
6. Wait no more than 15 seconds for the acknowledgement (shown on
screen) and send the following voice message on Channel 16 on high power.
PAN PAN, PAN PAN, PAN PAN
ALL STATIONS, ALL STATIONS, ALL STATIONS
__ COASTGUARD, __ COASTGUARD, __ COASTGUARD
THIS IS ______________, ______________, ______________,
(NAME OF VESSEL SPOKEN THREE TIMES)
CALL SIGN ________________ MMSI __________________
MY POSITION IS ____________________________________
(BY LAT & LONG, OR BEARING AND DISTANCE FROM A CHARTED OBJECT)
WE HAVE __________________________________________
I REQUIRE_________________________________________
(STATE NATURE OF URGENCY IE. MEDICAL ADVICE, TOWING ETC.)
I HAVE _____ PERSONS ON BOARD
ANY OTHER INFORMATION _____ ie, TYPE OF VESSEL, HULL COLOUR, ETC.
OVER
OR