Keep this notice near your VHF DSC Radio

VESSEL NAME

…………..………………….
MMSI …....….......…...…...…....
CALL SIGN ......…....….…..
SECURITE
ONLY TO BE USED IN THE CASE OF SAFETY MESSAGE CONCERNING THE
SAFETY OF NAVIGATION, SUCH AS OBJECT ADRIFT OR SEAMARK OFF
STATION.
1. Ensure radio is switched on.
2. Press CALL or MENU button.
3. Press ALL SHIPS button.
4. Select SAFETY CALL.
5. Press SEND button.
6. Wait no more than 15 seconds for the acknowledgement (shown on
screen) and send the following voice message on Channel 06 on high power.
SECURITE, SECURITE, SECURITE
ALL STATIONS, ALL STATIONS, ALL STATIONS
__ COASTGUARD, __ COASTGUARD, __ COASTGUARD
THIS IS ______________, ______________, ______________,
(NAME OF VESSEL SPOKEN THREE TIMES)
CALL SIGN ________________ MMSI __________________
MY POSITION IS ____________________________________
(BY LAT & LONG, OR BEARING AND DISTANCE FROM A CHARTED OBJECT)
WE HAVE LOCATED _________________________________
(TEXT OF SAFETY BROADCAST IE. OBJECT ADRIFT OR SEAMARK OFF STATION ETC.)
KEEP SHARP LOOKOUT
OUT

OR